## Slide 1: COAL Chapter 3
Week 3
Shoaib Rauf
Courtesy: Dr. Muhammad Nouman Durrani

## Slide 2: Basic Program Execution Registers
Registers are high-speed storage locations directly inside the CPU, designed to be accessed at much higher speed than conventional memory
There are eight general-purpose registers, six segment registers, a processor status flags register (EFLAGS), and an instruction pointer (EIP)

## Slide 4: General-Purpose Registers:
The general-purpose registers are primarily used for arithmetic and data movement.
As shown in Figure 2–6, the lower 16 bits of the EAX register can be referenced by the name AX
Portions of some registers can be addressed as 8-bit values
  For example, the AX register, has an 8-bit upper half named AH and an 8-bit lower half named AL

## Slide 5
The remaining general-purpose registers can only be accessed using 32-bit or 16-bit names, as shown in the following table:

## Slide 6: Specialized Uses of general-purpose registers
Some general-purpose registers have specialized uses:
• EAX (accumulator) - favored for arithmetic operations.
  It is automatically used by multiplication and division instructions
EBX (Base) - Holds base address for procedures and variables
ECX - The CPU automatically uses ECX as a counter for looping operations
EDX (Data) - Used in multiplication and division operations

## Slide 7: Index Registers
Index Registers contain the offsets for data and instructions.
Offset- distance (in bytes) from the base address of the segment.
• ESP (extended stack pointer register) contains the offset for the top of the stack to addresses data on the stack (a system memory structure)
• ESI and EDI (extended source index and extended destination index ) points to the source and destination string respectively in the string move instructions
• EBP is used to reference function parameters and local variables on the stack

## Slide 8
Segment Registers:
  In real-address mode, 16-bit segment registers indicate base addresses of pre-assigned memory areas named segments.
  In protected mode, segment registers hold pointers to segment descriptor tables (The descriptor describes the location, length and access rights of the memory segment).
  Some segments hold program instructions (code), others hold variables (data), and another segment named the stack segment holds local function variables and function parameters.
Instruction Pointer :
  The EIP, or instruction pointer, register contains the address of the next instruction to be executed.
  Certain machine instructions manipulate EIP, causing the program to branch to a new location.

## Slide 9: EFLAGS Register:
The EFLAGS register consists of individual binary bits that control the operation of the CPU or reflect the outcome of some CPU operation.
  A flag is set when it equals 1; it is clear (or reset) when it equals 0.
Programs can set individual bits in the EFLAGS register to control the CPU’s operation
For example: Interrupt when arithmetic overflow is detected

## Slide 11
The Status flags reflect the outcomes of arithmetic and logical operations performed by the CPU.
Parity- is set if the least-significant byte in the result contains an even number of 1 bits. It used to verify memory integrity.

## Slide 12: Integer Constants

## Slide 13: Integer Expressions
An integer expression is a mathematical expression involving integer values and arithmetic operators
The integer expression must evaluate to an integer, which can be stored in 32 bits (0 through FFFFFFFFh)

## Slide 20: Directives
Commands that are recognized and acted upon by the assembler
  Not part of the Intel instruction set
  Used to declare code, data areas, select memory model, declare procedures, etc.
  not case sensitive
Different assemblers have different directives
  NASM not the same as MASM, for example
myVar DWORD 26 ; DWORD directive, set aside
; enough space for double word
Mov eax, myVar ; MOV instruction

## Slide 22: Instructions
An instruction is a statement that becomes executable when a program is assembled.
Assembled into machine code by assembler
Executed at runtime by the CPU
We use the Intel IA-32 instruction set
An instruction contains:
  Label (optional)
  Mnemonic (required)
  Operand (depends on the instruction)
  Comment (optional)
Basic syntax
  [label:] mnemonic [operands] [ ; comment]

## Slide 25: Labels
Act as place markers
  marks the address (offset) of code and data
Follow identifier rules
Data label
  must be unique
  example: myArray (not followed by colon)
  count DWORD 100
Code label
  target of jump and loop instructions
  example: L1: (followed by colon)

## Slide 26: Mnemonics and Operands
Instruction Mnemonics
  memory aid
  examples: MOV, ADD, SUB, MUL, INC, DEC
Operands
  constant 96
  constant expression 2 + 4
  register eax
  memory (data label) count
Constants and constant expressions are often called immediate values

## Slide 27: Instruction Format Examples
No operands
  stc ; set Carry flag
One operand
  inc eax ; register
  inc myByte ; memory
Two operands
  add ebx, ecx ; register, register
  sub myByte, 25 ; memory, constant
  add eax, 36 * 25 ; register, constant-expression

## Slide 34
.data
promptUse byte "Enter two integers: ", 0
results byte "Result is: ", 0
.code
main proc
mov esi, offset array
mov ecx, int_count
l1:
mov edx, offset promptUser
call writestring
call readint
mov [esi],eax
add eax, [esi]
add esi, type dword
loop l1
mov edx, offset results
call writestring
call writeint
exit
main endp
end main